## Slide 1: WING DESIGN – Calculation of Swf
AESP 415 – Aircraft Design Part I Basics
Dr. Wout De Backer
1000 Catawba St, Ste 120
wdbacker@cec.sc.edu
4
MODULE
Lecture 15
TOPIC 8

## Slide 2: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Swf/S : Ratio between reference wing flapped surface and reference wing surface
The LE flapped area Swf_LE is generally larger than the TE flapped area Swf_TE
The flapped area Swf IS NOT the area of the flap!
You CANNOT have Swf = S due to presence of the fuselage (& ailerons)!
Swf_TE
Swf_LE
Fuselage
Notes: The area of the flap can be calculated by assuming that flaps have same taper ratio as the wing (quite common), knowing the value of cf/c and deciding at what distance from the fuselage intersection to locate the flaps.

## Slide 3: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Step 1: Determine the required flapped surface Swf to meet the required ΔCLmax
Estimate the flap hinge angle on the base of the position of the support spar (the back spar) used to attach the flaps
See values table next slide
α
clean
flapped
Notes: You can estimate the flap hinge angle value on the base of the position of the support spar (the back spar) used to attach the flaps.
Once a certain type of flaps has been selected and the required value for ΔCLmax has been estimated, the flapped surface can be estimated.
Rather than guessing a value of Swf/S, you can better solve the equation above computing the necessary Swf/S for a certain ΔClmax .
If the value of Swf/S result so large that you do not have space anymore for ailerons, then you can increase the chord length of the flap (if you are allowed) and/or change type of flaps.

## Slide 4: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Step 1: Determine the required flapped ΔClmax
Note: ΔClmax ≠ ΔCLmax
ΔClmax values in the order of 60-80% of those in the table should be used at take off, to account for the partial deployment of the devices
High lift device | ΔClmax when full deployed
TE devices (flaps) | 
Plain and split | 0.9
slotted | 1.3
fowler | 1.3 c’/c
Double slotted | 1.6 c’/c
Triple slotted | 1.9 c’/c
LE devices | 
Fixed slot | 0.2
Leading edge flap | 0.3
Kruger flap | 0.3
Slat | 0.4 c’/c
Notes: The c’/c value is related to the assumed value of cf/c, the ratio between the length of the flap chord and the airfoil chord. See next slide for the exact relation.
When assuming a value for cf/c, you are somehow deciding also the position of the wing back spar (the spar where flaps are hinged).
Too high values of cf will force you to move the back spar too much forward. You will have to check if enough volume is available for the fuel tanks!
Without considering the reduction of torsion stiffness of the wingbox…

## Slide 5: 8.4 Evaluation of the Lift Curve for the Flapped Wing
c’/c is dependent on flap type and deflection:
To compute c’/c, you can use this graph
First assume a value of cf (see note previous slide)
Then obtain Δc/ cf, based on deflection angle δf Note that Δc/ cf varies at take off and landing)
The flapped chord c’ is then:
c’= c + Δc

## Slide 6: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Step 2: Determine the approximate variation of α0L due to TE devices
Δα0L can be assumed to be the same value for various TE devices
α
clean
flapped
= - 15 deg at landing
= - 10 deg at take off

## Slide 7: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Step 3: Determine the slope of the flapped curve
For TE devices which do not increase the wing surface:
For TE devices which increase the wing surface: Where S’ is the increased wing surface by the extended flap (S’/S >1)
α
clean
flapped
Extracted flaps
S’
Swf
With*
Notes: To compute S’ you need to know the size of your flaps!
*If we assume for the flaps (or slats) the same taper ratio as the wing, by simple geometric considerations we can approximate: S’/S= 1+Swf/S(c’/c -1).
Concerning the curve part of the flapped lift curve (around the Clmax values, hence in correspondence of the stall angle), for simplicity we can assume the same shape as for the clean wing!

## Slide 8: 8.4 Evaluation of the Lift Curve for the Flapped Wing
Step 4: Add the contribution of the LE devices
See step 1 and table to compute the LE devices contribution
consider the increase in lift-curve slope due to the extended wing surface if slats are used no other LE devices increase the wing surface), exactly as explained for the flaps at step 3
Generally Δα0L associated to LE devices is neglected (only the TE devices are responsible of Δα0L )
α
clean
flapped
The LE flapped area Swf_LE is generally larger than the TE flapped area Swf_TE
Notes: See step 1 and relative table to compute the LE devices contribution.
Also here you can consider the increase in lift-curve slope due to the extended wing surface if slats are used (no other LE devices increase the wing surface), exactly as explained for the flaps at step 3.
Generally Δα0L associated to LE devices is neglected. As shown in figure above, only the TE devices are responsible of Δα0L .
Note that since the effect of the TE/LE devices depends on their deflection angles, we will get different CL-alpha-flapped curves at take off and landing`.. Typically we have full deflection during landing and about half of these value during takeoff (see typical values indicated in previous slides) in order not to spoil the aerodynamic efficiency of the wing during take off when there are climb gradient requirements to be met.

## Slide 9: 8.4 High Lift Devices Calculation of the flapped wing surface Swf
From the previous slides, we know that the flapped wing surface is defined as:
Now we know the % of the wing that is flapped, but how do we calculate the span wise flapped section lflaps?
Cr
Fuselage diameter d
b/2
Ct
lflaps
Cf,root
Cf,tip
lfroot
Swf_TE
Fuselage

## Slide 10: 8.4 High Lift Devices Calculation of the Swf
Consider a half wing with root chord cr , tip chord ct, and span b:
At any point x along the half wing, the chord cx , is defined as
Cr
Fuselage of diameter d
b/2
Ct
Cx
x

## Slide 11: 8.4 High Lift Devices Calculation of the Swf
At any point x along the half wing, the chord cx , is defined as:
For a flapped wing, with flaps starting at lf,root and a flap span of lflaps:
Cr
Fuselage diameter d
b/2
Ct
lflaps
Cf,root
Cf,tip
lf,root

## Slide 12: 8.4 High Lift Devices Calculation of the Swf
The flapped wing surface for this half wing is then:
Substitution of Cf,root and Cf,tip from previous slide yields:
Cr
Fuselage diameter d
b/2
Ct
lflaps
Cf,root
Cf,tip
lf,root

## Slide 13: 8.4 High Lift Devices Calculation of the Swf
Derivation:
Substitution

## Slide 14: 8.4 High Lift Devices Calculation of the Swf
Derivation:
Solve for lflaps

## Slide 15: 8.4 High Lift Devices Calculation of the Swf
The flapped wing surface for this half wing is then:
Solving for lflaps yields:
Cr
Fuselage diameter d
b/2
Ct
lflaps
Cf,root
Cf,tip
lf,root

## Slide 16: WING DESIGN
AESP 415 – Aircraft Design Part I Basics
Dr. Wout De Backer
1000 Catawba St, Ste 120
wdbacker@cec.sc.edu
4
MODULE
Lecture 15
TOPIC 8
Thank You!