## Slide 1: PRELIMINARY PROPULSION SIZING 1
AESP 415 – Aircraft Design Part I Basics
Dr. Wout De Backer
1000 Catawba St, Ste 120
wdbacker@cec.sc.edu
3
MODULE
Lecture 9
TOPIC 7

## Slide 2: Are you on track for this course?
Have you generated concepts for your requirements?
Have you worked on your CAD models (generating/annotating technical drawings)?
Have you completed the “inside-out” cross-section fuselage design process?
Have you started writing assignment 1 (Due soon)!
Notes: https://www.youtube.com/watch?v=AF55oyAJDBk

## Slide 3: Lecture Contents
Preliminary Propulsion Sizing
  7.1. Introduction
  7.2. Gas Generators
  7.3. Gas Turbine Thermodynamics (Recap)
  7.3.1 Ideal Cycle
  7.3.2 Gas Power & Efficiency
  7.3.3 Real Processes
  7.4. Gas Turbine Classifications & Configurations
  7.5. Governing Equations of Gas Turbines
  7.6. Engine Scaling techniques
  7.6.1 Piston Engine Scaling
  7.6.2 Propeller Engine Scaling
  7.6.3 Turbojet Engine Scaling
  7.6.4 Effects of Altitude and Velocity
  7.7. Engine Manufacturers & Joint Programs
  7.8. Future Developments
Notes: Contents from this slide deck is sourced and adapted from Aircraft Design 1 Course. Content by Dr. Arvind. G. Rao and prof J.P. van Buijtenen from Delft, University of Technology

## Slide 4: 7.1 Introduction
Balloon Analogy:
Imagine a balloon

## Slide 5: 7.1 Introduction
Balloon Analogy:
Escaping air acceleration Cs
Reaction balloon acceleration Co
Releasing air creates a propulsive reaction
Notes: Pressure in and out
An Area through which the air escapes.
Note mdot is flow rate (kg/s) and c_s = stream/escape velocity and c_0 is reaction velocity (m/s)

## Slide 6: 7.1 Introduction
Balloon Analogy:
Escaping air acceleration Cs
Reaction balloon acceleration Co
Adding external air supply creates endurance
Notes: Now imagine we magically attach a compressor to it and add air as it escapes

## Slide 7: 7.1 Introduction
Balloon Analogy:
Escaping air acceleration Cs
Reaction balloon acceleration Co
Electricity
Combining the supply with the balloon
motor
Notes: Put the compressor in front

## Slide 8: 7.1 Introduction
Balloon Analogy:
Fuel
Escaping air acceleration Cs
Reaction balloon acceleration Co
Fuel driven turbine system within the balloon
Notes: Make it a fuel-based compressor

## Slide 9: 7.1 Introduction
Balloon Analogy:
Escaping air acceleration Cs
Reaction balloon acceleration Co
Fuel
Increasing mass flow increases acceleration
Notes: Turbofan, bypass

## Slide 10: 7.1 Introduction
A pure jet engine:
Equivalent piston cycles:
Notes: Suck squeeze bang blow

## Slide 11: 7.1 Introduction
A pure jet engine:

## Slide 12: 7.1 Introduction
Components of a propulsion system:
Energy carrier
Power generator
Thrust generator
Energy carrier
Fuel Type | Energy density | Pollution
Kerosene | 43 MJ/Kg | High
Hydrogen | 120 MJ/kg | Moderate
Electric (Batteries, e.g. Lithium Ion) | 2 KJ/kg | Low
Fuel Cells | 3 KJ/kg | Low
Power generators
Type | Power Range | Speed Range (Mach) | Power to Weight (KW/kg) | Efficiency (%)
Military Aircraft Engine | < 15 MW | Up to Mach 2 | 10 | 25
Large Turbofans | < 50 MW | < Mach 1 | 5 | 35
Micro Gas Turbines | < 5 KW | < Mach 1 | 2 | 7
Turbo Props | < 10 MW | < Mach 0.7 | 5 | 35
Electric Motors | < 100 KW | < Mach 0.7 | 3 | 90
Internal Combustion Engines | < 500 KW | < Mach 0.7 | 0.6 | 30
Wankel engines | < 100 KW | < Mach 0.7 | 2.5 | 20

## Slide 13: 7.1 Introduction
Propulsion system & energy storage types
Piston engine
600W/kg
NiCAD battery
50-75 Wh/kg
Li-Ion battery 260-270 Wh/kg
Electric motor
3 KW/kg
Fuel cell
39 kWh/kg
Gas turbine
5 KW/kg
Kerosene
?? kWh/kg
Notes: What is the energy density of kerosene? 12 kWh/kg for kerosene

## Slide 14: 7.1 Introduction
Why a gas turbine?
Mercedes-Benz CLS-class
270 KW (362 HP)
Tesla Model S
515 KW
GE 9X (B777)
47000 KW per engine
1 GE 9X engine has the power of 91 Tesla Model S (sports)cars
Notes: Who here drives an SUV? Takes a cruise?

## Slide 15: 7.1 Introduction
Fuel (in gallons) per passenger carry a passenger for 350 miles:
Notes: Time in hrs

## Slide 16: 7.1 Introduction

## Slide 17: Lecture Contents
Preliminary Propulsion Sizing
  7.1. Introduction
  7.2. Gas Generators
  7.3. Gas Turbine Thermodynamics (Recap)
  7.3.1 Ideal Cycle
  7.3.2 Gas Power & Efficiency
  7.3.3 Real Processes
  7.4. Gas Turbine Classifications & Configurations
  7.5. Governing Equations of Gas Turbines
  7.6. Engine Scaling techniques
  7.6.1 Piston Engine Scaling
  7.6.2 Propeller Engine Scaling
  7.6.3 Turbojet Engine Scaling
  7.6.4 Effects of Altitude and Velocity
  7.7. Engine Manufacturers & Joint Programs
  7.8. Future Developments
Notes: Contents from this slide deck is sourced and adapted from Aircraft Design 1 Course. Content by Dr. Arvind. G. Rao and prof J.P. van Buijtenen from Delft, University of Technology

## Slide 18: 7.2 Gas Generators
A gas generator generates power in the form of hot pressurized gas (gas power)
Generating Gas Power
  Conversion of available energy in fuel to gas power (Gas generator)
Generating Thrust Power
  Conversion of gas power into propelling jet, increase momentum of the gas flow) (Propeller, Jet, Rotor)

## Slide 19: 7.2 Gas Generators
A gas generator generates power in the form of hot pressurized gas (gas power)
Gas power
Shaft power
Kinetic power
Direct
Indirect
Bypass engines
Turbofans
Turbojets
Generators
Pumps
Rotors
Propellers

## Slide 20: Lecture Contents
Preliminary Propulsion Sizing
  7.1. Introduction
  7.2. Gas Generators
  7.3. Gas Turbine Thermodynamics (Recap)
  7.3.1 Ideal Cycle
  7.3.2 Gas Power & Efficiency
  7.3.3 Real Processes
  7.4. Gas Turbine Classifications & Configurations
  7.5. Governing Equations of Gas Turbines
  7.6. Engine Scaling techniques
  7.6.1 Piston Engine Scaling
  7.6.2 Propeller Engine Scaling
  7.6.3 Turbojet Engine Scaling
  7.6.4 Effects of Altitude and Velocity
  7.7. Engine Manufacturers & Joint Programs
  7.8. Future Developments
Notes: Contents from this slide deck is sourced and adapted from Aircraft Design 1 Course. Content by Dr. Arvind. G. Rao and prof J.P. van Buijtenen from Delft, University of Technology

## Slide 21: 7.3 Gas Turbine Thermodynamics (Recap)
From your propulsion class:
Notes: 1-2 compression, energy is the shaded area
2-3 boom
3-4 out
h enthalpy is a function of temperature H = E + PV.
According to the law of energy conservation, the change in internal energy is equal to the heat transferred to, less the work done by, the system
S = entropy
V volume
p pressure

## Slide 22: 7.3.1 Ideal Cycle
Assumptions for the ideal cycle:
Ideal gas with constant cp and cv and constant composition
Constant mass flow
Compression and expansion is adiabatic and reversible (i.e. isentropic)
No pressure losses
No energy loss per component
1st law of thermodynamics:
With Q = input heat
W = Output power
m = mass
T = temperature [K]
S = entropy
Notes: 1 -> 2 is vertical

## Slide 23: 7.3.1 Ideal Cycle
1st law of thermodynamics:
Leads to:
  Compression stage
  Heat supply stage
  Expansion 1 stage
  Expansion 2 (Gas generator power)
  Heat Discharge stage
Notes: Work done, providing work
Providing heat

## Slide 24: 7.3.1 Ideal Cycle
Power balance in an ideal cycle:
And if we set that:
We get that:
Now, assuming mass flow and cp are equal:
Solve for Tg
=
u
Notes: Gamma = Cp/CV (ratio of specific heats for the gas)
T_g=T_3 - T_2 + T_1
=T_3-T_1 ((T_2/T_1 ) - T_1 / T_1 )
=T_3-T_1 ((P_2/P_1 )^((γ-1)/γ) - T_1/T_1 ) (where the relation for adiabatic compression was used T_2/T_1= (P_2/P_1 )^((γ-1)/γ) )

## Slide 25: 7.3.2 Gas power & Efficiency
Rearranging:
Then, from the ideal gas law:
Rearranging
Substitution

## Slide 26: 7.3.2 Gas power & Efficiency
Specific Power can be defined as:
With thermodynamic efficiency defined as:

## Slide 27: 7.3.2 Gas Power & Efficiency
The specific power is maximal when:
This is when all heat is taken out at the turbine:
Then:
And:
Note that:
Notes: Maximize the area, the green area is maximized

## Slide 28: 7.3.3 Real Processes
In real processes there will be losses (non-isentropic):
Notes: Non-ideal vs ideal

## Slide 29: Lecture Contents
Preliminary Propulsion Sizing
  7.1. Introduction
  7.2. Gas Generators
  7.3. Gas Turbine Thermodynamics (Recap)
  7.3.1 Ideal Cycle
  7.3.2 Gas Power & Efficiency
  7.3.3 Real Processes
  7.4. Gas Turbine Classifications & Configurations
  7.5. Governing Equations of Gas Turbines
  7.6. Engine Scaling techniques
  7.6.1 Piston Engine Scaling
  7.6.2 Propeller Engine Scaling
  7.6.3 Turbojet Engine Scaling
  7.6.4 Effects of Altitude and Velocity
  7.7. Engine Manufacturers & Joint Programs
  7.8. Future Developments
Notes: Contents from this slide deck is sourced and adapted from Aircraft Design 1 Course. Content by Dr. Arvind. G. Rao and prof J.P. van Buijtenen from Delft, University of Technology

## Slide 30: 7.4 Gas Turbine Classifications & Configurations
Typical Engine Configurations:
Turbojet
  All air passes through combustion chamber
Turbofan
  Bypass ratio
  Mixed vs. separate exhaust nozzles
Turboprop
  Propeller + (limited amount of) exhaust jet thrust)
  Free vs. fixed power turbine (single vs. twin shaft)
Single vs. multiple shaft engines
Notes: Efficiency vs speed.
Ram effect in turboprop/fan/bypass

## Slide 31: 7.4 Gas Turbine Classifications & Configurations
Typical Engine Classifications:
Turboshaft (-prop) Engine Configurations
Jet Engine Configurations
Notes: Turboshaft, primarily compression and acceleration in the prop. Energy comes from the turbine

## Slide 32: 7.4 Gas Turbine Classifications & Configurations
Typical Engine Classifications:

## Slide 33: 7.4 Gas Turbine Classifications & Configurations
Typical Engine Classifications:
Pure jet engine
Jet Engine with core bypass

## Slide 34: 7.4 Gas Turbine Classifications & Configurations
Main engine stations:
Intake
Compressor (axial/radial)
Combustor (annular, can type)
Turbine (axial/radial)
Afterburner/reheat
Nozzle & Exhaust

## Slide 35: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Compressor (axial/radial)
Radial compressor
Axial compressor
Notes: Don’t require a flow reversal in an axial compressor
Stator vanes drop velocity, clean flow and increase pressure

## Slide 36: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Combustor
Typical requirements for the combustor are:
  Must provide high combustion efficiency over wide operating conditions
  Low pressure loss over the combustion system
  Stable combustion over wide range of inlet conditions and mass flow
  Reliable starting/relight capability
  Minimum size/length/weight
  Low cost and good durability, maintainability, reliability
  Long operating life/long engine life
  Stable combustor exit temperature/flow pattern (for longer engine life)
  Multi-fuel capability (flexibility)
Notes: Highly compressed flow enters the combustor
Operating conditions: Flow during take-off/landing/cruise/climb
Jet A1, ethanol
Discuss picture, flow. Part of the flow is cooling. Left to right

## Slide 37: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Combustor
The combustor has liners to actively cool itself
Combustor Zones:
Primary zone
  Anchors the flame
  Provides sufficient time, temperature and turbulence for mixing
Secondary Zone
  Used to stabilize and complete combustion reaction processes
General air flow pattern

## Slide 38: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Can-type Combustor
Oldest form
Simple development
Strong
Easy maintenance/assembly
Notes: Can and annular, can is isolated combustion types

## Slide 39: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Annular Combustor
Compact
Good temperature distribution
Notes: “automatic relight”
Losing a can would upset the symmetry, causing vibrational issues

## Slide 40: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Turbine
Turbine blades are actively cooled, and are very complex parts
Notes: Minimum power out of the flow to keep the engine running,

## Slide 41: 7.4 Gas Turbine Classifications & Configurations
Engine Components: Turbine
Notes: 3d printing, channels and complexity, (lost wax casting and cnc machining)

## Slide 42: 7.4 Gas Turbine Classifications & Configurations
Early Jet Engines: Frank Whittle, inventor of the turbojet engine
Whittle GlosterE28 configuration
Whittle’s patent (1932)
Whittle’s can-type combustor
Notes: Rotary compression and turbine, flow has lots of bends

## Slide 43: 7.4 Gas Turbine Classifications & Configurations
Turbojet Engines:
Single spool turbojet with axial compressor

## Slide 44: 7.4 Gas Turbine Classifications & Configurations
Example turboprops:

## Slide 45: 7.4 Gas Turbine Classifications & Configurations
Examples: Helicopter Turboshaft

## Slide 46: 7.4 Gas Turbine Classifications & Configurations
Turbofan Engines:
Notes: Much more efficient, relative velocity (see propulsion class)

## Slide 47: 7.4 Gas Turbine Classifications & Configurations
Military Turbofan Engines with afterburner:
F100-PW-220 (F-15 / F-16)
F119-F22, F-135 - JSF
Notes: Isotropic line moves up, very inefficient
Vector nozzle

## Slide 48: 7.4 Gas Turbine Classifications & Configurations
High-bypass turbofan Engines: Stations
Notes: Example high-bypass turbofan. Transonic is to be avoided by slowing down flow and ram effect
Geared down turbofan slowing down the front blade allowing more energy to go in without breaking the sound barrier

## Slide 49: 7.4 Gas Turbine Classifications & Configurations
High-bypass turbofan Engines (twin spool):

## Slide 50: 7.4 Gas Turbine Classifications & Configurations
High-bypass turbofan Engines (triple spool):

## Slide 51: 7.4 Gas Turbine Classifications & Configurations
Examples: Ramjet (J58 for SR71)
Notes: “During engine start, rising fuel pressure in the fuel control signaled the ignition system that a metered amount of TEB could be injected into the engine combustion section, after the pilot moved the throttle from cut-off to the idle position. Preceded slightly by fuel, the TEB (triethylborane) exploded and ignited the JP-7.”

## Slide 52: 7.4 Gas Turbine Classifications & Configurations
Examples: Scramjet
Notes: On 27 September 2021, DARPA announced successful flight of its Hypersonic Air-breathing Weapon Concept scramjet cruise missile.[30] Another successful test was carried out in mid-March 2022 amid the Russian invasion of Ukraine. Details were kept secret to avoid escalating tension with Russia, only to be revealed by an unnamed Pentagon official in early April.[31][32]

## Slide 53: 7.4 Gas Turbine Classifications & Configurations
Why so many different engines?
Notes: Electric engines?

## Slide 54: 7.4 Gas Turbine Classifications & Configurations
Why so many different engines?

## Slide 55: Lecture Contents
Preliminary Propulsion Sizing
  7.1. Introduction
  7.2. Gas Generators
  7.3. Gas Turbine Thermodynamics (Recap)
  7.3.1 Ideal Cycle
  7.3.2 Gas Power & Efficiency
  7.3.3 Real Processes
  7.4. Gas Turbine Classifications & Configurations
  7.5. Governing Equations of Gas Turbines
  7.6. Engine Scaling techniques
  7.6.1 Piston Engine Scaling
  7.6.2 Propeller Engine Scaling
  7.6.3 Turbojet Engine Scaling
  7.6.4 Effects of Altitude and Velocity
  7.7. Engine Manufacturers & Joint Programs
  7.8. Future Developments
Notes: Contents from this slide deck is sourced and adapted from Aircraft Design 1 Course. Content by Dr. Arvind. G. Rao and prof J.P. van Buijtenen from Delft, University of Technology

## Slide 56: 7.4 Gas Turbine Classifications & Configurations
Why so many different engines?

## Slide 57: 7.5 Governing Equations of Gas Turbines
Thrust parameters:
Gross thrust:
Net thrust:
Specific thrust:
Dimensionless metric of thrust: or
Notes: C = speed
Non-dimensionalize as much as possible

## Slide 58: 7.5 Governing Equations of Gas Turbines
Fuel Consumption parameters:
Specific fuel consumption:
Dimensionless metric of thrust: or
Notes: Sfc = ambient velocity / total efficiency * heat capacity
R specific gas constant

## Slide 59: 7.5 Governing Equations of Gas Turbines
Effect of bypass ratio on thrust and thrust specific fuel consumption (TSFC):
Bypass Ratio [-]
Net Thrust [kN]
Notes: Trends with bypass ratio,

## Slide 60: 7.5 Governing Equations of Gas Turbines
Power-related parameters:
Propulsive jet power:
Thrust power:
Power loss

## Slide 61: 7.5 Governing Equations of Gas Turbines
(In-)efficiencies:
Chemical Energy
Heat
Gas Power
Kinetic Energy
Jet Power
Notes: Lot of conversions of energy, these are all theoretical. Other forms (boundary drag) also exist.
1. Efficiency of the combustion 2. work done by gas generator / mass flow and change in temperature 3. power of the gas going out / work done by gas generator

## Slide 62: 7.5 Governing Equations of Gas Turbines
(In-)efficiencies:
Jet Engine Power, Sankey diagram

## Slide 63: 7.5 Governing Equations of Gas Turbines
With Losses
Ideal Processes
(In-)efficiencies:
Notes: Comparing with losses against ideal processes

## Slide 64: 7.5 Governing Equations of Gas Turbines
Variation of propulsive (In-)efficiencies:

## Slide 65: 7.5 Governing Equations of Gas Turbines
During flight, the available power has to overcome the drag requirements:
Notes: Min power required and min drag power.
What if power required if the velocity moves to zero?
In helicopters a certain power is required for hover

## Slide 66: PRELIMINARY PROPULSION SIZING 1
AESP 415 – Aircraft Design Part I Basics
Dr. Wout De Backer
1000 Catawba St, Ste 120
wdbacker@cec.sc.edu
3
MODULE
Lecture 9
TOPIC 7
Thank You!